## Slide 1: Detection of Improvised Explosive Devices using Neutron Activation and Gamma Spectroscopy
MSci Viva Presentation Slides
Ryan D. Travers
HEPH-Hassard-2
22/03/2018
1

## Slide 2: Introduction
X-ray imaging is commonly at airports and seaports
High processing speeds and ease of operation
Difference in the attenuation used to discriminate between different materials
Impossible to discriminate between plastic explosives and bag of flour [1]
High false positive and negative rates
Hasn’t thwarted a single terrorist plot since their introduction [2]
Is there an alternative technology for the detection of explosives?
HEPH-Hassard-2
22/03/2018
2

## Slide 3: What is Neutron Activation and Gamma Spectroscopy?
14.1MeV Neutrons produced by the D-T reaction are used to assay a sample of material
Interact with atomic nuclei via the inelastic scattering interaction (n, n’ )
Energy of emitted gamma-ray photons depends on the nuclear band structure of the elements
Characteristic photons used as fingerprint for elemental composition of the sample
HEPH-Hassard-2
22/03/2018
Si-28 Neutron Cross Sections [3]
3

## Slide 4: Geant4 Simulations
Gean4 is a toolkit for the passage of particles through matter using Monte Carlo Methods
Handles geometry of the detection environment, tracking of particles and response of particle detectors
Spherical sample at the origin
4𝛑 spherical shell detector
Simulations initialised with collimated beam of 50 or 100 million 14MeV neutrons fired towards sample
HEPH-Hassard-2
23/03/2018
4
Detector
Sample
Neutron beam

## Slide 5: Two Methods for Determining the Elemental Composition
Method 1: Take inspiration from the ability of the human eye to discriminate between millions of different colours
Ratios between the intensity measured by three receptor cells are used to determine the colour
Method 2: Artificial Neural Network (ANN) with supervised learning
Finds mapping function
HEPH-Hassard-2
22/03/2018
5
Sensitivity of human cone cells [4]

## Slide 6: Method 1: The Spectrum Filter Approach
Use spectrum filters to alter the response function of gamma-ray detectors
Different transmission coefficients as a function of photon energy
Ratio between the intensity of radiation measured by each detector used for energy discrimination
Do such spectrum filters exist in the MeV range?
HEPH-Hassard-2
22/03/2018
6

## Slide 7
HEPH-Hassard-2
22/03/2018
Method 2: Machine Learning Approach
Artificial Neural Network with supervised learning
Training and prediction phase
Multi-channel pulse height analysers split spectrum into energy bins
Limit on resolution is 1keV
Maps the photon counts onto the elemental compositions
1
2
3
.
.
.
N-1
N
Input: photon counts
of Nth energy bin
H (%)
C (%)
N (%)
O (%)
7

## Slide 8: Results 1: Spectrum Filters Approach
Researched 28 elements ranging from to
Precluded radioactive elements ( and non-solid materials at RTP
Cross sectional data taken from the literature [5]
Photon absorption cross sections at 2MeV, 4MeV and 6MeV
Elements labelled according to which energy the photons had the highest transmission ratio
HEPH-Hassard-2
22/03/2018
8

## Slide 9
HEPH-Hassard-2
22/03/2018
Total photon absorption cross section lowest at for and at for
No element had its lowest cross section at
No spectrum filter appropriate found for the lower energies
9

## Slide 10
HEPH-Hassard-2
22/03/2018
Thicknesses, , calculated for , and
: ratio between the transmission ratios for photons with the smallest and second smallest absorption cross sections
10

## Slide 11
HEPH-Hassard-2
22/03/2018
Thicknesses used to calculate transmission ratios:
Exponential attenuation means signal cannot be separated from statistical fluctuations
Attenuations | N=1.5 | N=2
Z=13 (Al) | 9.2E-2 | 1.7E-2
Z=82 (Pb) | 1.6E-4 | 3.3E-7
11

## Slide 12
HEPH-Hassard-2
22/03/2018
Ideal spectrum filters have a narrow acceptance window
Measure defined as:
for and too low for effective photon discrimination
12

## Slide 13: Results 2: Machine Learning Approach
Simulations in Geant4 to produce gamma-ray spectra for BGO and HPGe detectors
Gaussian smearing to model detector response function
Asymmetric least squares method for baseline subtraction
65 permutations covering 4D space of H, C, N and O
Predictive capabilities of the ANN tested with 10 explosives and 10 benign materials
False positives and negatives have been calculated for each detector
HEPH-Hassard-2
22/03/2018
13

## Slide 14: Results 2: BGO
HEPH-Hassard-2
22/03/2018
Constant resolution of 10% taken from experimental data [6]
Unable to resolve some characteristic gamma-ray peaks
No resolvable Hydrogen peak effected accuracy of predictions
Photon counts split into bins of 20keV from 0.6MeV to 14MeV and inputted into ANN
14

## Slide 15: Result 2: HPGe
HEPH-Hassard-2
22/03/2018
Much smaller resolution () due to narrow band gap of Germanium [7]
Inputs of ANN taken as the 15 sets of bins centred at the characteristic gamma-rays peaks
15

## Slide 16: ANN Predictions with BGO and HPGe
HEPH-Hassard-2
22/03/2018
16

## Slide 17: Results 2: Predictive capabilities of the ANN
HEPH-Hassard-2
22/03/2018
HPGe gives much better predictions for the elemental compositions
Resolution has a large effect on the accuracy of ANN predictions
* Error =
is the difference between the predicted and actual percentage composition of Hydrogen
 | Error*
BGO | 
HPGe | 
 | Error*
BGO | 
HPGe | 
17

## Slide 18
HEPH-Hassard-2
22/03/2018
False negative and positive detection rates calculated for BGO (left) and HPGe (right) as a function of warning radius
18

## Slide 19: Practical Challenges
HPGe kept at 77K to prevent thermal excitation of electrons from the valence to conduction band
Constant supply of liquid Nitrogen coolant
Neutrons are highly penetrative and so lots of shielding needed
More research into the average processing time for each scan
Can the costs of the detection system be justified?
HEPH-Hassard-2
22/03/2018
19
Semiconductor | Band gap at 300K (eV)
Ge | 
Si | 
Semiconductor | Band gap at 300K (eV)
Ge | 
Si | 
Concentration of electrons in the conduction band,

## Slide 20: Bibliography
[1] Zentai, G. (2008). X-ray imaging for homeland security. Imaging Systems and Techniques, 2008. IST 2008. IEEE International Workshop on, 1-6.
[2] Khan, F. N. (2017). Is That Airport Security Scanner Really Safe? Scientific American. [online]. Available from: https://blogs.scientificamerican.com/observations/is-that-airport-security-scanner-really-safe/ [Accessed 20/03/2018].
[3] Hodgson, Lohstroh, Sellin, & Thomas. (2017). Neutron detection performance of silicon carbide and diamond detectors with incomplete charge collection properties. Nuclear Inst. and Methods in Physics Research, A, 847, 1-9.
[4] Stockman, A. & Sharpe, L. Human cone spectral sensitivities: a progress report. Vision Research, 1998, Vol.38(21), pp.3193-3206.
[5] Hubbell, J., Gimm, et al. (1980). Pair, Triplet, and Total Atomic Cross Sections (and Mass Attenuation Coefficients) for 1 MeV‐100 GeV Photons in Elements Z =1 to 100. Journal of Physical and Chemical Reference Data, 9(4), 1023-1148.
[6] S. Lam, M. Gascón, S. Podowitz, S. Curtarolo and R. S. Feigelson, "Nonproportionality and Scintillation Responses of LSO:Ce From 4.3 to 300 K," in IEEE Transactions on Nuclear Science, vol. 60, no. 2, pp. 993-999, April 2013.
[7] Calligaris, L., Massironi, A. & Presotto, L. (2006/2007). Gamma Spectroscopy. Available at: http://virgilio.mib.infn.it/labdida/lib/exe/fetch.php?id=laboratorio_di_fisica_delle_particelle&cache=cache&media=relazionelaboratoriogamma.pdf [Accessed 21/03/2018].
[8] (2006). Gamma Interactions: Photoelectric Effect and Pair Production. Lecture notes in Applied Nuclear Physics, MIT. [online] Available from: https://ocw.mit.edu/courses/nuclear-engineering/22-101-applied-nuclear-physics-fall-2006/lecture-notes/lec20.pdf [Accessed 21/03/2018].
[9] Compton Scattering. Lecture delivered on 25th October 2006. Available at: http://lappweb.in2p3.fr/~maire/tutorials/compton.pdf [Accessed 21/03/2018].
HEPH-Hassard-2
22/03/2018
20

## Slide 21: Appendix
HEPH-Hassard-2
22/03/2018
21

## Slide 22: Results 2: Raw Predictions Data
HEPH-Hassard-2
22/03/2018
22

## Slide 23: Appendix: Geant4 Environment
Density:
Sample radius:
Detector thickness:
Distance between detector and origin:
Mass:
HEPH-Hassard-2
22/03/2018
23

## Slide 24: Baseline Correction: Asymmetric Least Square Method
Square error loss function is given different weights depending on whether the residual is positive or negative
Combines smoothing, , and asymmetry, , parameters
Appropriate for when deviations from the baseline predominantly occur on one side, e.g., in gamma-ray spectroscopy
HEPH-Hassard-2
22/03/2018
24

## Slide 25: Detector Response: Resolution
Gaussian full-width at half maximum (FWHM):
Resolution given by:
In semiconductor detectors, fluctuations in the number of charge carriers follows a sub-Poissonic probability distribution due to the introduction of phonon transitions
Introduce the Fano factor, :
and is the mean energy for the electron-hole creation
HEPH-Hassard-2
22/03/2018
25

## Slide 26: Neutron Interactions:
Scattering interactions:
  Elastic scattering (n, n’)
  Inelastic scattering (n, n’ )
Absorption interactions:
  Radiative capture (n, )
  Absorption of a neutron and release of other secondary particles: (n, xn’), (n, ), (n, p), (n, D) etc.
Nuclear fission
HEPH-Hassard-2
22/03/2018
26

## Slide 27: Cross sections for photon interactions
Cross section for the photoelectric effect [8]:
has been experimentally determined to be between and
Pair production cross section with shielding [8]:
Cross section for Compton scattering for large photon energies [9]:
HEPH-Hassard-2
22/03/2018
27

## Slide 28: BGO and HPGe Cross Sections
HEPH-Hassard-2
22/03/2018
*Partial Compton scattering cross sections: secondary electrons with an energy within 1keV from the Compton Edge
28

## Slide 29: General Features of Gamma Spectra
HEPH-Hassard-2
22/03/2018
Compton Edge, , corresponds to backscattered photons:
29

## Slide 30: HPGe Gamma Spectrum
HEPH-Hassard-2
22/03/2018
30

## Slide 31: Definitions of Detection Rates:
HEPH-Hassard-2
22/03/2018
 | Positive | Negative
Presence |  | 
Absence |  | 
 | Positive | Negative
Presence |  | 
Absence |  | 
31

## Slide 32
HEPH-Hassard-2
22/03/2018
32